## Slide 1: Running Neural Networks on the NIC
FACULTY OF
COMPUTER SCIENCE
Siracusano, G., Galea, S., Sanvito, D., Malekzadeh, M., Haddadi, H., Antichi, G., & Bifulco, R. (2020). Running Neural Networks on the NIC. arXiv preprint arXiv:2009.02353.

## Slide 2
Presentation Outline
Introduction
Contribution
Motivation
Neural Networks on the NIC
Implementation
Use Cases
Evaluation
Discussion and Conclusion

## Slide 3
Introduction
N3IC relies on Quantization
3 network-based applications:
  Traffic Classification
  Anomaly Detection
  Network tomography
NICs with integrated programmable components
Previous works:
  Load balancing
  Consensus Protocols
  Key-Value stores
Challenges of Machine Learning applications in the NIC:
  They need more resources
  They need complex operations
PCIe data transfer overheads

## Slide 4
N3IC: an approach to accelerate NN inference
Implementing N3IC in three ways
A compiler that generates P4 code from a Neural Network
Checking three use cases
Contribution

## Slide 5
I/O operations are expensive
Observation 1: Running NN inference on a NIC could completely avoid crossing the PCIe bus and help in the execution of time sensitive workloads.
Motivation

## Slide 6
NN processing is memory bounded
Observation 2: FC layers have relatively low arithmetic intensity. This makes hardware architectures optimized for fast memory accesses a good fit for their execution.
Motivation

## Slide 7
NICs processing load depends on traffic patterns
Observation 3: The relatively small arithmetic intensity of MLPs aligns well with the potentially available processing power of a NIC.
Motivation

## Slide 8
The need for small NN models
  Quantization
The need for a low complexity algebra
  Bitwise logic, shifts, and simple integer arithmetic operations
The need for hardware compatibility
The Solution: Binarization
Original NN  NN with 0 or 1 weights
Neural Networks on the NIC

## Slide 9
SoC NIC: Netronome NFP4000:
  Tens of Micro Engines (ME)
  MEs are programmed using microC
  CLS is used for N3IC (~100ns access time)
From NNs to P4:
  NNtoP4
Porting P4 to NetFPGA
  Translating P4 to HDL (Verilog)
Implementation

## Slide 10
Traffic Classification: Dataset: UPC-AAU, 750K flows, P2P or not
Anomaly Detection: Dataset: UNSW-NB15, 170K flows, good or bad
Network Tomography: CLOS-like Fat Tree datacenter network in NS3
Use Cases

## Slide 11
Testbed:
  Host: Intel Haswell E5-1630 v3, 3.7GHz
  NIC1: Netronome Agilio CX SmartNIC, with an NFP4000 processor, 800MHz
  NIC2: NetFPGA-SUME, 200MHz
  Under test NIC is connected to DPDK packet generator with 40Gbps cables
Evaluation

## Slide 12
Traffic Analysis
Result 1: when performing traffic analysis, N3IC saves at least an entire CPU core, while providing a 1.5x higher throughput and 10-100x lower processing latency than a system running on the host’s CPU.
Evaluation

## Slide 13
Network Tomography
Result 2: compared to a host-based system, for low throughput but latency-sensitive use cases N3IC-FPGA can reduce processing latency by 20x. This enables applications like SIMON to run in real time in networks running at 400Gb/s and beyond.
Evaluation

## Slide 14
Neural Network Size
Result 3: N3IC-NFP’s and N3IC-FPGA’s processing throughput decreases linearly, while latency increases linearly, with the NN size. N3ICP4 does not scale to larger NNs.
Evaluation

## Slide 15
NIC Resource usage
Result 4: N3IC-FPGA consumes a very small fraction of the NetFPGA resources, and both N3IC-FPGA and N3IC-NFP can be configured to trade-off used NICs’ resources with provided performance.
Evaluation

## Slide 16
N3IC Costs:
  Converting NN models with Binarization
  Application should be split
N3IC-FPGA is more efficient.
Large NN cannot be implemented with N3IC
Discussion

## Slide 17
N3IC Features:
  N3IC provides 1.5x higher throughput
  100x lower latency
  Uses only 2% of resources
  N3IC-FPGA is more efficient.
Conclusion

## Slide 18
Any Question?